## Slide 1: Colliders – Lecture VS2: Collective Effects (BB, SC, etc) Incoherent Effects (halo, cool)
Vladimir Shiltsev, Northern Illinois University
part of the “Colliders” class by V.Shiltsev, J.Eldred and B. Simmons
Muon Collider School · Aug. 04 – Aug 07, 2025 · U. Chicago

## Slide 2: Important Beam Effects
Beam-beam effects
Space-charge effects
Instabilities
Collimation
Cooling
Diffusion and Intrabeam scattering
Beamstrahlung
Polarization
Synchrotron radiation
etc etc etc (20 – 40 topics at USPAS/CAS)

## Slide 3: Beams as Moving Charges
Beam is a collection of charges
Represent electromagnetic potential for other
charges
Forces on itself (space-charge, wake-fields/impedances) and opposing beam (beam-beam effects)
  Main limit for present and future colliders
  Important for high density beams, i.e. high intensity and/or small beams = for high luminosity !

## Slide 4: EM Forces in Beams: self fields Bθ=βEr
same charges repel each other (opp attract) F=eE
same currents attract each other (opp repel) F=βeB=-β2eE
Qualitatively: Balance of These Forces
1
+Q
+J
2
-Q
+J
FE=(+Q,-Q) attracts
FB=(+J,+J) attracts
2
+Q
-J
both FE FB repel
beam-beam
1
+Q
+J
FE=(+Q,+Q) repels
FB=(+J,+J) attracts
Total FE - FB repels
= FE - β 2FE = FE /γ2
space-charge
2
+J
1
+Q
+J
FE=(+Q,-Q) attracts
FB=(+J,-J) repels
Diff FE - FB attracts,
eg skin-eff ΔF ~ FE
induced fields
1
-J
-Q
conducting surface
δ
R

## Slide 5: BEAM-BEAM (1)

## Slide 6: Beam-Beam Effects
A beam acts on particles like an electromagnetic lens, but:
  Does not represent simple form, i.e. well-defined multipoles
  Very non-linear form of the forces, depending on distribution
  Can change distribution as result of interaction (time dependent forces ..)
Results in many different intensity dependent effects and problems:
  unstable betatron oscillations
  growth of beam sizes
  particle losses

## Slide 7: Beam-Beam Fields: Start with a Cylinder
i.e. force is linear inside, nonlinear outside

## Slide 8: Kick from a Round Gaussian Beam

## Slide 9: Beam-beam kick in reality
Deflection scan (LEP measurement)
  linear inside
  const outside

## Slide 10: Beam-beam Detuning with Amplitude
Non−linear force 
tune depends on the amplitude of betatron oscillations
large effect for A<sigma
small effect for A>>sigma

## Slide 11: Linear tune shift - two dimensions
“bare lattice” tune
“bare lattice” tune + linear shift due to beam-beam (=core particles)

## Slide 12: Non-linear tune shift in two dimensions
core
halo

## Slide 13: e+e- LEP vs p-pbar collider Tevatron
3
3
30
30
980
0.28
0.28
0.012 x2 IPs
Tevatron

## Slide 14: Observations (Reality of Beam-Beam)
Remember:
Luminosity should increase
for:
Beam-beam parameter should increase
But:

## Slide 15: Beam-Beam Limits : e+e- Colliders

## Slide 16: Beam-beam Limit on Luminosity
First - Beam−beam parameter increases linearly with intensity
Saturation above some intensity
Then – luminosity increases only linearly with N above the so−called
beam−beam limit

## Slide 17: What’s happening?
Above beam-beam limit: σy increases when N increases
  to keep constant  equilibrium emittance !
Therefore:
is NOT a universal constant !
  depends on tunes/WPs, damping rates, etc
  difficult to predict exactly for hadron machines

## Slide 18: Beam-Beam Limits: pp/pbar Colliders
Tevatron Collider Run II

## Slide 19: Tevatron Tune Footprint “Confinement”
7th order resonances:
Q=4/7=0.571 -
HIGH LOSSES
12th order resonances:
Q=7/12=0.583 -
BAD BEAM LIFETIME
5th order resonances:
Q=3/5=0.600 –
EMITTANCE BLOWUP
p
pbar
protons
antiprotons

## Slide 20: Resonances matter! … Diffusion
Tune map: LHC (simul)
Shown resonances up to order 20
Amplitude map: LHC (simul)
Shown diffusion rates vs Ax/Ay
Measure tune of a particle based on (here) 4096 turns -Calculate linear change over 10 measurements, separated by 10k turns

## Slide 21: Non-linear Resonances
Nonlinear terms in the force F(x,y,t)~x^l y^p δ(t-kT) lead to appearance of driving terms oscillating with frequencies mQx+nQy, and therefore open opportunities for nonlinear resonances if
mQx+nQy=p
|m|+|n| is order
of the resonance
i.e. resonance diagram up to
fourth order; importance of the resonance depends on the force shape and order (low order = more serious; often longitudinal deviations matter if mQx+nQy +lQs =p
harmonics of
ωx
ωy
ω0

## Slide 22: How to control beam-beam effects?
Find 'lenses' to correct beam-beam effects
Head on effects: force is ~r
  Linear "electron lens" to shift tunes
  Non-linear "electron lens" to reduce spread
  Successful e-lenses at FNAL and RHIC
Long range effects:
  At very large distance: force is ~1/r
  Same force as a wire !
Overall - success with active compensation

## Slide 23: Attempt #1: Four beams e-e+ e-e+
four-beam collider Dispositif de Collisions dans l’Igloo (DCI, 1970s) at Orsay with two 0.8 GeV electron beams and two positron beams of the same energy, all meeting at the same interaction point (J.LeDuff et al)
Q1+Q2+Q3+Q4=0
J1+J2+J3+J4=0
E=B=0

## Slide 24: Attempt #1: Four beams compensation
No improvement of performance was obtained in the four-beam configuration compared to collisions of just two beams of electrons and positrons.
A transverse dipole feedback as well as a
detuning of the two rings did not help.
The compensation is believed to be unsuccessful due to the loss of beam stability, both for dipole and higher order modes of coherent motion.

## Slide 25: Approach #2: Electron lens
Protons focus pbars +
Electrons defocus
Net effect = zero
Footprint compressed
e- profile same as p+
(V.Shiltsev et al)

## Slide 26: Electron Lens Compensation
“…to compensate (in average) space charge forces of positively charged protons acting on antiprotons in the Tevatron by interaction with a
negative charge of a low energy high-current electron beam “ (V.Shiltsev, 1997)
electron beam

## Slide 27: Some Facts on Electron Lenses
~4 mm dia 2 m long very straight beam of ~10kV ~1A electrons (~1012) immersed in 3T solenoid
generates strong radial electric field E ~ 0.3MV/m

## Slide 28: Tevatron Electron Lens #1 (F48)

## Slide 29: TEL2 in the Tevatron Tunnel (A11)

## Slide 30: Compensation with Two TELs
Tev Run II: 36x36 bunches in 3 trains
compensate beam-beam tune shifts
  a) Run II Goal
  b) one TEL
  c) two TELs
  d) 2 nonlinear TELs
requires
  1-3A electron current
  stability dJ/J<0.1%
  e-pbar centering
  e-beam shaping
b
d
c
a
Yu.Alexahin

## Slide 31: Electron Charge Distribution
Electron gun
Shiltsev et al., PRL 99, 244801 (2007). Shiltsev et al., NJP 10, 043042 (2008).
G. Stancari, et al., (2011)
Phys. Rev. Lett. 107, 084802

## Slide 32: TEL e-beam aligned and timed on protons
in space
in time
P12
P11
P10
P9
A24
TEL
Transverse e-p alignment is very important for minimization of noise effects and optimization of positive effects due to e-beam. Timing is important to keep protons on flat top of e-pulse – to minimize noise and maximize tune shift.

## Slide 33: Tevatron Electron Lenses (2001-2011)
Technology proven, tune shift ~0.01 demo’d
First successful active compensation
Head on effects compensation:
  Reduced emittance growth of a PACMAN antiproton bunch (“scallops” effect)
Long range effects compensation:
  Significant (x2) improvement of the lifetime of most affected proton bunches
    By shifting tunes of otherwise unfavorable bunch away from resonances

## Slide 34: Tuneshift dQhor=+0.009 by TEL
Three bunches in the Tevatron, the TEL acts on one of them

## Slide 35: “Scallops” in Pbar Bunch Emittances
95% normalized vertical emittance, pi mm mrad
Bunch #
Too close to
Qy=0.6

## Slide 36: Emittance Growth of A33 Suppresed by TEL
Store #2540
May 12, ‘03
A33
1  mm mrad/hr
-TEL on it
A21
2.2  mm mrad/hr
A9
4.1  mm mrad/hr

## Slide 37: TEL2 on One Proton Bunch P12
When TEL off:
bunches #12 and #24
have same lifetime of
8.7 hrshrs=11%/hr loss
When TEL on:
bunch #12 lifetime
is ~2x #24 lifetime:
17.4 hrs vs 10.0 hr

## Slide 38
Approach #3: Head-On Comp’n in RHIC
With e-lens, one can compensate Head-On effect: not only the tune footprint, but also the resonant driving terms if elens is placed 180 degrees (betatron phase) away from the main IP (one IP compensation)
(W.Fischer et al)

## Slide 39: RHIC pp 2015 elens Success

## Slide 40: RHIC pp 2015 elens in Ops
With 0.6A, 2.1m long, 5 kV e-beam, essentially:
- one out of 2 IP head-on effect cancelled,
max allowed beam intensity increased by ~40%,
peak average lumi ~tripled, averaged lumi ~ doubled

## Slide 41: Approach #4 : Wire Compensation of Long Range Beam-Beam Interactions
Fields of separated p+ beam:
E~NIPs Np /d
B = E
Field of separated conductor (wire):
E=0
B~2Je /d
Combined effects of p+ beam + e- beam will cancel out if
wire is placed at the same d
wire kick Jxlength matches NIPsNp
(J.P.Koutchouk, G.Sterbini et al)

## Slide 42: Wire Compensation in the LHC (2018)
Proton losses in collisons are due to:
Luminosity burn up dN/dt=-Lx80 mbarn
and beam-beam effects -
different for regular and PACMAN bunches
So, plotted is dN/dt/Lumi
for regular and PACMAN bunches

## Slide 43: Beam-beam topics also include…
Beam-beam effects in linear colliders
Beamstrahlung
Asymmetric beams
Synchrobetatron coupling
Crabbed and crab-waist schemes
Monochromatization
Beam-beam simulation codes
... etc.

## Slide 44: BREAK (!...?) SPACE-CHARGE EFFECTS

## Slide 45: Intense Beams : Forces and Losses (1)
eE
Electric Force Repels
p+
p+
eB(v/c)=eE(v/c)2
Magnetic Force Attracts
Net Force: Repels
eE-eE(v/c)2 =eE (1- β2)=eE/γ2

## Slide 46: Intense Beams : Forces and Losses (2)
N
Fmax~eN/σ2γ2
Defocusing Force is Non-linear
F
r
Space-charge effects (emittance growth, losses):
proportional to current (N)
scale inversely with beam size (σ)
scale with time at low energies (γ)
Linacs 5-20 MeV/m
Rings 0.002-0.01 MeV/m

## Slide 47
47
Space-charge: Core vs Tail
J. Eldred Transverse Dynamics Accelerators
47
S. Lund
Notes: 47
47
47

## Slide 48: Space-charge effects: Proton Rings
SC tune shift

## Slide 49
Space-charge Tune-spread & Betatron Resonances
49
JPARC MR:
M. Friend
G. Franchetti et al.
PRSTAB 2017
Notes: 49
49
49
49

## Slide 50: Max SC tuneshift Achieved: -0.2…-0.5

## Slide 51: Ways to Increase “Protons Per Pulse”
Increase the injection energy:
  Gain about Np~ βγ2, need (often - costly) linacs
Flatten the beams (using 2nd harm, RF) :
  Makes SC force uniform, Np~ x2
“Painting” beams at injection:
  To linearize SC force across beams Np~x1.5
Better collimation system beams:
  From η~80% to ~95% Np~x1.5
Make focusing lattice perfectly periodic:
  Eg P=24 in Fermilab Booster, P=3 in JPARC MR  Np~ x1.5
(to be tested) Introduce Non-linear Integrable Optics :
  May reduce the losses and allow Np~ x 1.5-2
(tbt) Space-Charge Compensation by electron lenses :
  Electrons to focus protons, may allow Np~x1.5 - 2

## Slide 52: Beams Document 6790-v1 FNAL
Space-Charge Compensation R&D

## Slide 53: IOTA: Integrable Optics Test Accelerator @ FNAL
E-Lens
RF
Octupoles
NL Magnet
Lambertson
Kickers
injected beam
C=40 m
150 MeV/c e- and 70 MeV/c p+
OSC insert

## Slide 54: (COHERENT BEAM) INSTABILITIES

## Slide 55: Instabilities
Beam instabilities are driven by the electromagnetic interaction with the accelerator environment (-> wakefields/impedances) and by electron clouds.
Above a certain intensity threshold the beam’s oscillation amplitude increases exponentially and the beam is either lost at the wall (transverse instabilities) or from the RF bucket (longitudinal) and/or the emittance increases.
Presently, heat loads and instabilities are one of the main beam quality and intensity limitation in particle accelerators for high intensity and brightness !
Finding “cures” for instabilities is one of the major challenges in beam physics and accelerator technology for future machines.
High energy beams: Beam instabilities are a ‘current effect’. However, synchrotron radiation, photoelectrons or other high energy effects affect instability thresholds.

## Slide 56: Maxwell’s equations and Lorentz Force
EM forces due to : a) wake fields and impedances, b) electron cloud, c) beam-beam, d) etc
See more in USPAS lectures

## Slide 57: Wake-fields

## Slide 58: Wake-fields - Examples
Wake fields behind a bunch generated at a step-out transition from a small to a larger beam pipe

## Slide 59: What if we have many particles
Wake-functions

## Slide 60: Even “simple” resistive wall leaves wakes
Key points: a) longitudinal wakefield leads to particle energy loss and pipe heating; b) transverse wake is defocusing for vacuum beam pipe (focusing in case of electron cloud)
“Skin-effect” – EM field
penetration
depth

## Slide 61: Consequences: two-particle model
In linacs: Beam-break up (BBU) instability
In rings: Head-tail instability (aka TMCI = Transverse Mode Coupling Instability)

## Slide 62: Intensity Limits and Cures
Beampipe heating is important for cryo – may limit on Nb Ib
Instabilities severely limit either single bunch current Ib or total beam current Nb Ib
Cures employed so far:
Reduce wakes/impedances – no discontinuities in beam pipe, better conducting materials, etc
In linacs – BNS damping= introduce energy difference btw head and tail of the bunch (RF phase choice) leading to slight difference in the betatron oscillation frequencies
In rings
  Feedback dampers (might not work for single bunch instabilities)
  introduce betatron frequency spread via chromaticity dQ=Q’(dP/P) (does not always work) or octupoles dQ~Oct*σ2 (mostly worked so far) or electron beams for Landau damping (next gen colliders)

## Slide 63: Intensity Limits and Cures
168 LHC octupoles for Landau Damping
Concern is that these octupolse are so nonlinear that they reduce Dynamic Aperture of the collider  affect lifetime

## Slide 64: Landay Damping by Electron Lenses

## Slide 65: Collimation
To protect from enormous beam power (and power density) of high energy accelerators and colliders – events and processes:
  Injection errors
  Instabilities
  Losses due to beam-beam, beam-gas, intrabeam scattering, etc
  Synchrotron radiation photons
Protect magnets, RF and detectors !

## Slide 66: Collimators
Tevatron 12 collimators:
  Hor and Vert
  Proton and antiproton
  4 primaries
    5 mm W
  8 secondaries
    1.5 m stainless steel
    Flat to <25 micron
    As close as few mm to the
Efficiency 95-99%
  reduction of background in CDF and D0 detectors x20-100
Protons
Damage to E03 1.5m Collimator
  see lectures NM1-4

## Slide 67: (Most Sophisticated) LHC Collimation
Efficiency > 99.99%
i.e. <0.01% escapes
dedicated absorbers

## Slide 68: Collimation Challenges and Cures
Too many, too close to beams  large wakefields/impedance
Can be damaged/destroyed …. NEW METHODS
Bent crystal collimation Hollow e-beam collimation
Makes bigger deflection  better interception of scattered particles
Tested at the Tevatron and LHC
Soft “penetrable” & fast diffusor  undamageable. Tested at the Tevatron and being built for LHC
Few mm Si (100)
100’s of μrad
Few Amperes, few mm dia, few m long e-beam

## Slide 69: Aperture and Dynamic Aperture
Collimators - losest to beam – 5-10’s of σ
Often coated (eg TiN) and/or grooved (ecloud)
Physical beam pipe ~60-100 mm …10’s-100’s σ
Often coated (eg TiN) and/or grooved (ecloud)
SKEKB
90mm
The dynamic aperture is the stability region of phase space in an accelerator – dependent on nonlinearities and chromatic effects
For proton machines - stability over O(1e9) turns
For electron/muon machines - stability over O(1e3) turns

## Slide 70: Beam Cooling
Beam Phase Space Density Increase
As needed for a collider
Forbidden by the Liouville theorem in non-dissipative systems
x,y,t
x’,y’,dP/P
Ideally - “6D-Cooling”
100 MeV electrons in IOTA ring

## Slide 71: Diffusion and Cooling (1)
Diffusion equation for beam distribution function f(J,t), J- action variable
In the presence of cooling:
where for example:

## Slide 72: Beam Cooling Methods to Date
Electron Cooling – since 1970’s
Widely used to cool ions and antiprotons
0.1 - 8 GeV/n (50 keV – 4 MeV electrons DC)
100 MeV electrons in IOTA ring
Synchrotron Radiation Damping – since 1960’s
common in all e+/e- rings
Stochastic Cooling – since 1970’s
Widely used to cool ions and antiprotons
0.1-100 GeV/n (up to 10 GHz feedback BW)
Laser Cooling – since 1990’s
Works for some highly charged ions
0.1-0.5 GeV/n, deep cooling, spectroscopy
Lectures VL13-14

## Slide 73: Recent Beam Cooling Breakthroughs
2019 - Ionization cooling of muons (140 MeV/c, RAL, UK)
MICE
~10% in one pass
2020 – “Bunched” electron cooling of ions (γ~5, BNL)
2025 – Coherent Electron cooling of ions (26.5 GeV/n, RHIC) – ongoing PoP exp’t at BNL
THz bandwidth
2021 – Optical Stochastic cooling e- (100 MeV, FNAL)
IOTA
THz bandwidth
RHIC
RF e-gun

## Slide 74
  Thanks for Your Attention !
Questions !?

## Slide 75: Literature
W.Herr, CAS school
https://cds.cern.ch/record/941319/files/p379.pdf
V.Lebedev, V.Shiltsev, Tevatron Book Ch.8
https://indico.cern.ch/event/774280/attachments/1758668/2915590/2014_Book_AcceleratorPhysicsAtTheTevatro.pdf
Proc. 2013 ICFA mini-workshop on "Beam-Beam Effects in Hadron Colliders"
https://indico.cern.ch/event/189544/
Past schools :
  A. Chao, The beam-beam instability, SLAC-PUB-3179 (1983).
  L. Evans, The beam-beam interaction, CAS Course on proton-antiproton
  colliders, in CERN 84-15 (1984).
  L. Evans and J. Gareyte, Beam-beam effects, CERN Accelerator School, Oxford
  1985, in: CERN 87-03 (1987).
  A. Zholents, Beam-beam effects in electron-positron storage rings, Joint
  US-CERN School on Particle Accelerators, in Springer, Lecture Notes in
  Physics, 400 (1992).

## Slide 76
Instabilities:
A.Chao, Physics of collective beam instabilities in high energy accelerators (1993) https://www.slac.stanford.edu/~achao/wileybook.html
Many useful articles:
S.Myers, H.Schopper Accelerators and Colliders
(2013, open access)
https://link.springer.com/book/10.1007/978-3-030-34245-6
Comprehensive JUAS-book (2371 pages – all topics!)
https://doi.org/10.23730/CYRSP-2024-003.

## Slide 77: Can also be used for Long-Range Beam-Beam Compensation
vary the currents bunch-by-bunch in two e-lenses installed at βx≠ βy
e-beam p-bars
Ie[A]
TEL1
TEL2
nbunch

## Slide 78: Beam-Beam Effects
Remember:
Overview: which effects are important for
present and future machines (LEP, PEP,
Tevatron, RHIC, LHC, ...)
Qualitative and physical picture of the effects

## Slide 79: Fields and Forces (1)
Start with a point charge q and integrate over the particle distribution.
In rest frame only electrostatic field: E≠0 while B=0
Transform into moving frame and calculate
Lorentz force
Note that F≈0 if velocities are collinear

## Slide 80: Fields and Forces (2)
Derive potential U(x, y, z) from Poisson equation:
The fields become:
Example Gaussian distribution:

## Slide 81: A Common Example: Gaussian
For 2D case the potential becomes:
Can derive E and B fields and therefore forces
Also easy for uniform distribution: E and B scale linear with r for r<a, and 1/r for r>a… easy for simple easily integrable axisymmetric distributions
For arbitrary distribution (non-Gaussian):
  difficult (or impossible, numerical solution required)

## Slide 82: Further Simplification: Round Gaussian
Round beams:
Only components Er and B are non-zero
Force has only radial component, i.e. depends only on distance r from bunch center, i.e.

## Slide 83: Beam-Beam Kick
Kick : - angle by which the particle is deflected during the passage
Derived from force by integration over the collision assume:
     Newton’s law

## Slide 84: Beam-Beam Kick
Using the classical particle radius:
we get radial kick and in Cartesian coordinates:

## Slide 85: Beam-Beam Kick
Kick(force) varies strongly with amplitude:
  linear inside  like quadrupole  tune shift amplitude independent at << sigma
  1/r outside the beam core  amplitude dependent tune shift
Highly nonlinear btw 1 and 3 sigma:
  contains many high order multipoles

## Slide 86: Beam-beam strength parameter  tuneshift
Slope of force at zero amplitude  proportional to (linear) tune shift from beam-beam interaction
This defines: beam-beam parameter
For head-on interactions we get:
so far: only an additional “quasi-quadrupole” BUT non-linear part of beam-beam force scales with
Note that for flat beams σx >>σy ξy >> ξx

## Slide 87: Tune Spectra: with/w.o. Beam-Beam
Non−linear force 
particles with different amplitudes
have different frequencies (tunes)
We get frequency (tune) spectra
Width of the spectra: ~ξ
Linear force 
all particles have same tune  one line in the spectrum of transverse oscillations
simulations
simulations

## Slide 88: In Reality – Even More Complex
Tevatron 980 GeV p and
980 GeV antiprotons (pbars)
Colliding with ξ~0.028
Force is focusing  tuneshift is positive
Measured with 21MHz Schottky monitors
RHIC 100 GeV p + 100 GeV p
Colliding with ξ~0.020
Force is de-focusing  tuneshift
is negative
Measured with BTF (beam transfer function) monitor
…more on that later

## Slide 89: Complications : Strong-Strong vs Weak-Strong
Both beams are very strong (strong-strong):
  Both beam are affected and change due to beam-beam interaction
  Examples: LHC, LEP, RHIC, ...
One beam much stronger (weak-strong):
  Only the weak beam is affected and changed due to beam-beam interaction
  Examples: SPS collider, Tevatron (early in Run II) , ...

## Slide 90: Incoherent vs Coherent Beam-Beam Effects
Incoherent (single particle effects):
  Single particle dynamics - treat as a particle passing through a static electromagnetic lens
  Basically, non-linear dynamics effects:
    unstable and/or irregular motion (“chaos”)
    beam size blow up or bad lifetime
    Very bad: unequal beam sizes (studied at SPS, HERA, Tevatron)
Coherent (bunches affected as a whole):
  Collective modes
  Bunch-by-bunch differences in:
    Orbits
    Tunes
    Chromaticities

## Slide 91: Coherent Beam-Beam: Modes
Coherent mode: two bunches are "locked" in a coherent oscillations
  0-mode is stable (Mode with NO tune shift)
  π-mode can become unstable (Mode with LARGEST tune shift)

## Slide 92: Coherent Beam-Beam: Modes
LEP
Two modes clearly visible
Can be distinguished by phase relation, i.e.
sum and dierence signals

## Slide 93: Coherent Beam-Beam: Flip-Flop
Bunch sizes get bigger or smaller out of phase
(PEP-II, VEPP-2000, etc)
The intensity threshold for the flip-flop depends on:
asymmetry in beam intensities
x-y coupling
3D Flip-Flop effects triggered by non-linearities of lattice. p-mode on 1/5 resonance. The effect have shown a strong sensitivity to X-Y coupling, beta unbalance and bunch length  main limitation in VEPP 2000.

## Slide 94: Multi-Bunch Operation: Need and Issues
How to collide many bunches (for high L) ??
Must avoid unwanted collisions !! Otherwise ξ2Bξ
Separation of the beams:
  Pretzel/helix scheme (SPS,LEP,Tevatron)
  Bunch trains (LEP, PEP)
  Crossing angle (LHC)

## Slide 95: Tevatron: 36 proton x 36 antiproton
Same beam pipe and
magnetic fields 
same orbits 
72 IPs
Need only 2
 separate at 70
 Electric field
396 ns bunch
separation
 59 m btw IPs

## Slide 96: Tevatron High Voltage Electrostatic Separators
300 kV over 50 mm gap; 3 m ; 24 of them (H/V)

## Slide 97: Tevatron Helix
size 12-15 mm
at 150 GeV
6-8 mm
at collisions
24 electrostatic
separators are used

## Slide 98: All beam indicators become bunch dependent due to long-range beam-beam effects
Orbits
Tunes, couplings
Chromaticities
In both – protons and pbars
Have 3-fold symmetry (trains of 12)

## Slide 99: Long-range B-B Seen at Low-Beta (980 GeV)
Bunch #1 Bunch #8
Synchrotron light monitors show 40 micron b-by-bunch hor pbar orbit variation along the bunch train with 3-train symmetry (4 microns for protons)
Also indicate coupling differences 

## Slide 100: Antiproton Vertical Orbit
In general – very good agreement btw simulations and measured Q, orbits, Q’s

## Slide 101: Pbar Bunch Tunes in Collisions

## Slide 102: Pbar Bunch Chromaticity in Collisions

## Slide 103: In the LHC
15+15 long range interactions (6-12 σ)
2808 p bunches in each beam, every 25 ns
Two beams in separate beam pipes except in common chamber around 4 experiments
Local separation via two horizontal and two vertical crossing angles

## Slide 104: Parasitic Beam-beam Kicks
For horizontal separation d:
In LHC 15 collisions on each side, 120 in total!
Effects depend on separation, eg tuneshift

## Slide 105: PAMCMAN bunches due to gaps
Average orbit and tune variations can be corrected, but:
LHC bunch filling not continuous: holes for injection, extraction, dump ..
“Only” 2808 of 3564 possible bunches circulate ! 1756 "holes"
"Holes" meet "holes" at the interaction point - But not always ...

## Slide 106: Effect of PACMAN bunches (end of train)
Some bunches can meet a hole/holes (at beginning and end of bunch train) 
They see fewer unwanted interactions in total: between 120 (max) and 40 (min) long range collisions  Different integrated beam-beam effect for different bunches
LHC

## Slide 107: Tune Spread - too large for safe operation

## Slide 108
108
Transverse Interaction of Co-Moving Charges
J. Eldred Transverse Dynamics Accelerators
108
Electric Repulsion:
Magnetic Attraction:
Weakened Repulsion with Acceleration:
Notes: 108
108
108

## Slide 109
109
Space-charge Core vs Tail
J. Eldred Transverse Dynamics Accelerators
109
Relativistic Distortion of EM Fields
“Pancake-ification”
Transverse space-charge forces much stronger than longitudinal space-charge.
Transverse and Longitudinal charge distribution can be written as separable functions:
Gaussian cylinder for a line-charge:
Notes: 109
109
109

## Slide 110
Tune Diagrams
J. Eldred Transverse Dynamics Accelerators
110
Notes: 110
110
110
110

## Slide 111
Summary
J. Eldred Transverse Dynamics Accelerators
111
The linear transverse dynamics of a particle accelerator are governed by Hill’s Equation, which is a time-varying harmonic oscillator.
We calculate the trajectory of individual particles through the many individual magnets of a particle accelerator using transfer matrices.
Transfer matrices are also used for the beam size and oscillation phase, which are represented by Courant-Snyder parameters.
There are chromatic effects, resonances, and space-charge effects that complicate the process of designing and operating a particle accelerator.
Some backup slides on longitudinal dynamics.
Notes: 111
111
111
111