## Slide 1: Colliders – Lecture VS1: Introduction: Accelerators Technologies and History Luminosity
Vladimir Shiltsev, Northern Illinois University
part of the “Colliders” class by V.Shiltsev, J.Eldred and B. Simmons
Muon Collider School · Aug. 04 – Aug 07, 2025 · U. Chicago

## Slide 2: Day 1: General
Lecture 1 Colliders - V.Shiltsev (NIU)
Lecture 2 Beam Optics – J.Eldred (FNAL)
Lecture 3 Beam Dynamics – V.Shiltsev
Homework: ~1 hrs in groups + 2 hrs together - V.Shiltsev, J.Eldred, B.Simmons (NIU)

## Slide 3: This School is “Just About Concepts”
…by no means even a comprehensive intro
US PAS : US Particle Accelerator School
https://uspas.fnal.gov/
CAS: CERN Accelerator School
https://cas.web.cern.ch/
Even better: sign up for undergrad/grad programs in accelerators (>10 in the US Univ.)

## Slide 4: This lecture

## Slide 5: Acceleration: Increase of Energy
Energy gain is F[force] x L[distance]
Forces: Strong/nuclear [local]
Electromagnetic [used widely]
Weak [??]
Gravitational [see next slide]

## Slide 6: Acceleration by the Fields of Gravity
…collisions between particles free falling from infinity and a disk of material plunging off the retrograde innermost stable circular orbit of a near-extremal Kerr black hole…  result in rest-frame energies at the level of 1 to 100’s of TeV (or more).

## Slide 7: ENERGY: Ideas / Breakthroughts
#1 Electrostatic E [10keV – 10 MeV ]
#2 Resonant/RF E [0.1 GeV – 1 TeV]
#3 Colliders Ecm [1 GeV- 14 TeV]
#4 Heavy leptons Epcm [10 - 100 TeV]
#5 Plasma Wakes E [0.1- 1 PeV]

## Slide 8: ACCELERATORS vs COSMOS
Flux (m2 sr s GeV)-1
Energy (GeV)
10 40
10 30
10 -20
1
10 10
10 20
10 -10
1
10 3
10 6
10 9
10 12
LHC
“Oh-My-God Particle”
(1991, Utah)
~45 orders of
magnitude in flux
~8 orders of magnitude in energy
Spectrum of Cosmic Rays

## Slide 9: Lorentz-Invariant Mandelstam Variables
s=E 2cme

## Slide 10: Kinematics of collisions
Two particles (E1,2 , m1,2) collide at angle θc
One particle stationary (E2 =m2 c2)
Both particles move (E1,2 >>m1,2 c2)
Gain for (E= 6500 GeV, m=0.936 GeV) is ~120 times (0.11 vs 13 TeV)

## Slide 11: Types of colliding beam facilities

## Slide 12: Colliders Landscape
61 years since 1st collisions
Spring 1964 AdA and VEP-1
31 operated since
(see RMP review)
7 in operation now
see next slides
2 under construction
NICA (2025) and EIC (2032)
At least 2 more types needed
Higgs/Electroweak factories
Frontier E >> LHC

## Slide 13: Colliders: Energy

## Slide 14: Only Electric Field Boosts Energy

## Slide 15: How much power is needed
Where “shunt impedance”:
“Quality factor”
~10^4 for Copper 300K
10^(9-10) for SC Nb cavities
“R/Q” cavity geometry factor
~100 for “open” elliptic cavities
196 Ohm for “pillbox” cvavity

## Slide 16: RF Cavities
Resonant cavity, eg “pill-box”:
R=10cm at fRF=1.14 GHz
Max gradient/voltage per cavity:
Is determined by RF power and shunt impedance
Is limited by breakdown or dark current radiation or loss of superconductivity
  depends on frequency, CW or pulse duration, geometry, material, temperature, etc
Max ~100 MV/m in normal-conducting cavities at 12 GHz
Max ~31.5 MV/m SRF cavities 1.3GHz
LEP-I 352 MHz
ILC 1300 MHz

## Slide 17: Rings vs Linacs
lower Vacc if you can

## Slide 18: Types of Circular Accelerators
Cyclotrons – 1930-40’s
  E.O.Lawrence (UCB)
E[GeV]=0.3 B[T] R[m]
R is fixed [4.24km LHC]
Betatrons – 1940-50’s
  D.Kerst (UI)
Synchrotrons (Tevatron, LHC, MuColl)

## Slide 19: Highest Energy = Highest Field SC Magnets
4.5 K He, NbTi
+ warm iron small He-plant
NbTi cable
cold iron
Al collar
NbTi cable
simple &
cheap
NbTi cable
2K He
two bores
4.5T
8.3T
3.5T
5.3T

## Slide 20: Key for Magnets: Current Density
Generation of a pure dipole
by a cos θ current distribution
Scaling: Bmax~ J/Aperture
(assume all A is filled by conductor)
J~j(current density) x A^2
Bmax~j x A
but Cost ~A^2 (cost of needed conductor) x length ~ A^2/B ~ ~A/j
Therefore, high(est) current density is needed to maxizmize B-field and
minimize Cost
  For room temperature copper j~(1-10) A/mm^2
  For superconductors  kA/mm^2

## Slide 21
Record fields attained with dipole magnets of various configurations and dimensions, and either at liquid (4.2 K, red) or superfluid (1.9 K, blue) helium temperature.
Nb-Ti
Nb3Sn
Superconducting wire critical current density versus magnetic field: three main materials Nb-Ti, Nb3Sn, HTS
Nb-Ti
Nb3Sn
HTS
L. Bottura
P. Lee
SC Magnets: Fields and Current Densities

## Slide 22
15 T dipole demonstrator
Staged approach: In first step pre-stressed for 14 T
Second test in June 2020 with additional pre-stress reached 14.5 T
60-mm aperture
4-layer graded coil
84% on the laodline at 1.9 K
92% on the loadline at 4.2 K
cosq dipole
SC Accelerator Magnets: Current Record 14.5T

## Slide 23: Focusing Beams with Quadrupole Magnets
Vertical Plane:
Horizontal Plane:
Luckily…
…pairs give net focusing in both planes! -> “FODO cell”

## Slide 24: Betatron Oscillations, Tune
As particles go around a ring, they will undergo a number of betatron oscillations ν (sometimes Q) given by
This is referred to as the “tune”
We can generally think of the tune in two parts:
Ideal orbit
Particle trajectory
64.31
Integer : magnet/aperture optimization
Fraction: Beam Stability
see Jeff’s lecture

## Slide 25: Particle Equations of Motion (1)
Solution:
So, tune:
see Jeff’s lecture

## Slide 26: Key beam parameter: Emittance
As a particle returns to the same point on subsequent revolutions, it will map out an ellipse in phase space – more in Jeff’s lecture
Area = e
β,γ, α - Twiss parameters
For an ensamble of particles:
Product size x angle X_rms x X’_rms is called emittance
Normalized emittance = emittance x gamma is an adiabatic invariant
Luminosity (tbd) ~ 1/ε

## Slide 27: Squeezed in ATLAS/CMS
Image courtesy John Jowett
Most Important Equations
β* | Sigma*
25 cm | 8 um
βtriplet | Sigma triplet
~5 km | 1.1 mm
σ’=32μrad
σ’=0.14μrad
Ɛn = 1.8 mm·mrad
Numerical Example: LHC
β | Sigma
~200 m | 0.23 mm
σ’=0.67μrad
Final Focus quads
~100 m from IPs
Regular LHC locations
in “arcs”
normalized emittance
rms beam size
rms beam
angular spread

## Slide 28: Particle Equations of Motion (2)
Also, note that nonlinear fields on beam orbit add complexity:
Beta-functions are defined by
Eg symmetric solution in free space (K=0):
More in Jeff’s lecture
especially at resonant frequencies
n=1 dipole
n=2 quadrupole
n=3 octupole
n=4,5,6…

## Slide 29
l
Collider Spot Size
to decrease the beam size
at the collision point we
can reduce either b* or e
s~b*
bunch
sz
beam
envelope
low-beta
quadru-
pole
b*:
must remain larger than sz (‘hourglass effect’)
quadrupole aperture must be respected

## Slide 30: Longitudinal Motion: Phase Stability
Nominal Energy
Particles with lower E arrive earlier and see greater V.
Particles are typically accelerated by radiofrequency (“RF”) structures. Stability depends on particle arrival time relative to the RF phase. Note: the speed is fixed = speed of light , so time of arrival depends only on the energy (in the bunch – energy deviation wrt “reference central particle”)
see Jeff’s lecture

## Slide 31: Example: LHC
RF Frequency 400 MHz
(35640 times revolution frequency)
RF Voltage = 8 cavities x 2 MV = 16 MV / turn (max)
In collisions dE/dn= 0 V/turn (synchronouse phase ~0)
Slow energy-position oscillations (23 Hz or ~500 turns)
rms energy spread 1.3e-4 (1GeV) rms bunch length ~ 8cm

## Slide 32: Scales of Time-scales/Frequencies
…even slower might be operational processes :
injection/extraction (1/sec… 1/min… 1/hr … 1/day)
beam cooling (sometimes - hours)
luminosity decay (min… days)

## Slide 33: BREAK (!...?)

## Slide 34: Luminosity
For (same size) Gaussian bunches:

## Slide 35: Luminosity: Unequal Bunches
yields:

## Slide 36: Correction for Crossing Angle and Offset
where:
Offset d1-d2≠0
≈1

## Slide 37: “Crab Crossing” Collisions
Note: either the crossing angle or amplitude of the crabbing affect instantaneous luminosity  can be used for “luminosity leveling”
Head-tail rotation by RF dipole deflectors (eg HL-LHC)

## Slide 38: Hour-Glass Effect
Same for
beam size
σz << β*
σz > β*

## Slide 39: Luminosity Reduction Due to Hourglass
For round beams, equal beta’s and no crossing angle, H-factor
In reality, beta* is often constant and bunchlength can grow leading to small decay of luminosity

## Slide 40: Luminosity Summary : Key Factors
Want it higher either smaller rings = higher B
or high rep linear collider (= power)
High E helps
This factor comes from adiabatic reduction of the rms beam size for the same emittance
Higher intensity drives L note that N(bunch) comes squared while # of bunches linear; sometimes N is limited by beam-beam, often nbN is limited  try to put all charge in one bunch
Smallest emittance that’s where most of beam physics goes to – cooling to stop heating, noises, dyna-mics in injectors, etc etc etc
Minimize beta need stronger focusing = larger aperture and stronger LB quads
Keep H under control keep bunch length and beta* more or less matched, be aware of the crossing angle (sometimes need it  crabs)

## Slide 41: Colliders: Luminosity
1ab-1/yr

## Slide 42: Colliders: Need More Luminosity vs Energy
future colliders
future
colliders

## Slide 43: Luminosity evolution
Factors change in time
Therefore, the lifetime

## Slide 44: LHC Lumi Lifetime (~7 hrs) and Integral

## Slide 45: Colliders : Most Important Topics/Effects
Engineering of magnets, RF, PSs, vacuum, sources, targets, diagnostics, collimators, etc
  Exciting science: new acceleration techniques/plasma
Beam physics
  One particle: beam optics, long-term stability, resonances, losses, noises, diffusion/emittance growth, etc
  One beam: instabilities, synchtrotron radiation, beam-induced radiation deposition, intrabeam scattering, cooling, space-charge effects and compensation
  Two-beams: beam-beam effects and compensation, beamstrahlung, machine-detector interface, etc
Assuming particle physics interest  choice of accelerator scheme depends on
  Readiness, cost and power consumption vs E, L reach  MuColl

## Slide 46: BREAK (!...?) Muon Colliders

## Slide 47: Colliding Leptons vs Hadrons
Protons
ECM partons≈ 2E × 0.1
E=γmc2
E=γmc2
ECM leptons=2E
Leptons
e+
μ+
τ+
e-
μ-
τ-

## Slide 48: Muon Colliders in the US
Muon Collider eg at FNAL μ+μ-
Circumference ~10 km, Ecm =3…10 TeV
NC+SC magnets and SRF
Cost ~12-18 B$ (ITF’21) 17±4 BCHF (IMCC’25)
20 yrs of R&D
*no labor, escalation, or contingency
circular
compact
low(er)cost
low(est) power consumption
 Fast production, cooling (size reduction)& acceleration
Muons decay quickly 2.2μs×γ
Fermilab site: about 3 x 4 miles, 6,800 acres

## Slide 49: Muon Colliders: Main Challenges
Muons are not stable particles
  Muon lifetime at rest (mc^2=0.105 GeV) is 2.2 microseconds
  Muon lifetime at 5 TeV (collider γ≈50000) is 100 milliseconds
  Muon can be made available only as secondary or tertrially particle, products of reactions like
    p(beam)+p(target) K,π  μ
    e+e-  μ+μ-
    γ + Ze  μ+μ-
That usually results in large emittance (large angular spread) muon beams and requires deep cooling for high Luminosity
Therefore, major challenges for High Luminosity MC are:
  Muon production
  Fast muon cooling
  Fast muon acceleration
  Neutrino flux hazard

## Slide 50: Muon Collider Parameter Table under development by the International Muon Collider Collaboration
RAST, Vol 10, No. 01, pp. 189-214 (2019)

## Slide 51: Average Luminosity of Muon Collider
NB: each muon makes ~300B[T] turns in a ring with average field B
scales with B, the total beam power Pb, and the beam brightness (the third factor above is the beam-beam ξ)
The beta-function at the two IPs scales as β*~1/γ within certain range of energies, giving overall scaling Lumi ~ γ2 with other limiting parameters fixed. The main challenges to luminosity achievement with decaying particles are related to production and fast cooling and acceleration of O(1012) muons per bunch without emittance degradation.

## Slide 52: (Explanatory to Previous slide)

## Slide 53: O(14 TeV) Muon Collider Sub-Systems (approx. to scale)

## Slide 54: Muon Collider Subsystems
(i) a high power proton driver (SRF 4 GeV 2-4 MW H- linac);
(ii) pre-target accumulation and compressor rings, in which high-intensity 1-3 ns long proton bunches are formed;
(iii) a liquid mercury target for converting the proton beam into a tertiary muon beam with energy of about 200 MeV;
(iv) a multi-stage ionization cooling section that reduces the transverse and longitudinal emittances and, thereby, creates a low emittance beam;
(v) a multistage acceleration (initial and main) system --- the latter employing a series recirculating rapid cycling synchrotrons (RCS) to accelerate muons in a modest number of turns up to 3-7 TeV using high gradient superconducting RF cavities;
(vi) about 8.5 km diameter collider ring located some 100 m underground, where counter-propagating muon beams are stored and collide over the roughly 1000--2000 turns corresponding to the muon lifetime.
* From the point of beam physics, complexity of a Muon Collider is
closer to that of the Tevatron (higher) than to that of the LHC (lower)

## Slide 55: Muon Production: 1-4 MW proton driver needed
see lectures by J.Eldred and D.Neuffer Tue

## Slide 56: MERIT Experiment – Demo of 4-8 MW Proton Targetry
At CERN PS
1e13 protons 24 GeV (115kJ/pulse)
Liquid Mercury target 20 m/s
15 T Solenoid
Measured disruption length = 28 cm
see R.Zwaska lecture Wed

## Slide 57: The Need for Muon Cooling
Muon Phase Space After Target
vs What’s Needed for Collider
x
x'
y
y'
t
dP/P
Need “6D-Cooling”

## Slide 58: Fast Cooling of Muon Beams
• The desired 6D emittance for a MC is 5-6 orders of magnitude less from the emittance of the beam at the target • How that can be done before muons decay?  ionization cooling: ionization loss along momentum followed by RF acceleration (restore energy) along longitudinal axis only (like in the Synchr Rad damping)
• Requires rf cavities to compensate for lost longitudinal energy • Use strong B-fields to confine beams
see K.Yonehara lecture Tue

## Slide 59: Equation:
(1st) Cooling term ~ (dE/ds) – larger the better
(2nd) Heating/ scattering term ~ beta-function at the absorber and 1/radiation length of the material (a low-Z preferred, Liquid Hydrogen, Li, LiH, Be)
Energy of muons

## Slide 60: Longitudinal DoF: rms E spread
fluctuations of ionization
energy losses
cooling term
Cooling requires that d(dEμ/ds)/dEμ > 0. But at energies below about 200 MeV, the energy loss function for muons, dEμ/ds, is decreasing with energy and there is thus heating of the beam. Above 400 MeV the energy loss function increases gently, thus giving some cooling, though not sufficient for fast cooling application (see previous slide).
The “struggling” term
increases as γ^2, and the cooling system size scales as γ  cooling at low energies is desired.
Energy spread can also be reduced by artificially increasing d(dEμ/ds)/dEμ by placing a transverse variation in absorber density or thickness at a location where position is energy dependent, i.e. where there is dispersion (= emittance exchange long transverse)

## Slide 61: MICE: Muon Ionization Cooling Experiment = 1 “cell”
ISIS 800 MeV
proton
synchrotron
@ RAL (UK)

## Slide 62: Muon 4D Cooling: MICE Results (2024)
Fig. 3 | Transverse emittance change measured by MICE. Emittance change between the TKU and TKD reference planes, Δε⊥, as a function of emittance at TKU for 140 MeV/c beams crossing the LH2 MICE absorbers. Results for the empty cases, namely, No absorber and Empty LH2, are also shown. The measured effect is shown in blue, whereas the simulation is shown in red. The corresponding semitransparent bands represent the estimated total standard error. The error bars indicate the statistical error and for some of the points, they are smaller than the markers. The solid lines represent the approximate theoretical model defined by equation (10) (Methods for the absorber (light blue) and empty (light pink) cases. The dashed grey horizontal lines indicate a scenario where no emittance change occurs.
https://doi.org/10.1038/s41567-024-02547-4

## Slide 63: 6D Ionization Cooling
Initial beam is narrow with some momentum spread
  Low transverse emittance and high longitudinal emittance
Beam follows curved trajectory in dipole
  Higher momentum particles have higher radius trajectory
  Beam leaves wider with energy-position correlation
Beam goes through wedge shaped absorber
  Beam leaves wider without energy-position correlation
  High transverse emittance and low longitudinal emittance
(Do transverse 4D cooling… and repeat the cycle)

## Slide 64: Rectilinear Ionization Cooling Channel
6D emittance reduction by 5 orders of magnitude
(between point 2 to 5).
Length ~ 900 m
Final cooling section design requires ~30 T solenoids (point 5 to 6)

## Slide 65: Full Ionization Cooling & Demonstrator
MC ionization cooling channel consists of ~800 muon cooling cells
The cooling of muons requires very compact assembly of normal conducting RF cavities, superconducting solenoids, and either liquid hydrogen or LiH absorbers
Large bore solenoids: from 2 T (D=1 m) to 20+ T (D=0.05 m)
RF cavities (300-800 MHz) must operate in multi-Tesla fields
Wedge-shaped absorbers must and large muon beam intensities
Schematic of the muon cooling demonstrator
https://doi.org/10.1140/epjc/s10052-023-11889-x
 | Muon mom. MeV/c | Total length, m | Total # of cells | Total RF voltage, MV | B_max, T | 6D emm. reduction | Beam loss, %
Full scale MC | 200 | ~980 | ~820 | ~15,000 | 2-14 | x 1/105 | ~70%
Demonstrator | 200 | 48 | 24 | ~260 | 0.5-7 | x 1/2 | 4-6%
The Muon Ionization Cooling Demonstrator Experiment:
■ Timeline: 2029-2034 ■ Location: Fermilab or CERN ■ Cost: 300 ? M$
see D.Stratakis lecture Wed

## Slide 66: Acceleration and Collider Ring ~75% of the MC Cost
Options (high low cost):
Linac (very costly!)
Recirculating linear accelerator (RLA)
Fixed field alternating gradient (FFA)
Pulsed synchrotrons
~14T Large Aperture Collider Magnets
Alexahin et al 2018 JINST 13 P11002
CBETA FFA at Cornell/BNL arXiv1706.04245

## Slide 67: The Idea of Pulsed Muon RCS
Rapid cycling synchrotron (RCS)
  Potentially larger acceleration range at affordable cost
  Could use combination of static superconducting and ramping normal-conducting or HTS magnets
  But have to deal with energy in fast pulsing magnets
Of course, circumference of the RCS will be larger than that of collider as AVERAGE max B-field in RCS < AVERAGE (static) B-field collider ring

## Slide 68: Need pulsed magnets dB/dt ~1000T/s
Approach to an economical magnet
is to use HTS tape: very low AC losses
in superconductor
Fermilab, 2021

## Slide 69: Neutrino Flux (Muons decay to e+ν ν )
Collider Ring design - see lecture of E.Gianfelice-Wendt on Wed

## Slide 70: Neutrino Radiation Dose & Control
<1 mSv/yr mitigation ideas:
depth
few mm vertical collider orbit variation (next slide)
few cm magnet positions float (next slide)
less muons… =smaller emittance to keep L
Cone gets narrower with energy
Cross section grows with energy
~ 1 m

## Slide 71: On Required R&D: μ-Coll Costs and Risks
 | Approx. % of the Total Cost | Approx. Luminosity Risk Factor
Proton Driver & Targetry | 15 - 20 % | 10 1 - 2
Muon Cooling | 10 - 15 % | 10 3 – 4
Acceleration | 30 - 60 % | 10 1 – 2
Collider | 25 - 40 % | 10 0 – 1
TOTAL | 12 - 18 B$ *ITF? | 10 5 - 9

## Slide 72: Ultimate Colliders Luminosity vs Energy
1 TeV
10 TeV
100 TeV
10 ab-1/yr
1 ab-1/yr
0.1 ab-1/yr
0.01 ab-1/yr
1 fb-1/yr
Parton CME
μ+μ− Circular
pp Circular
V.Shiltsev, “Ultimate Colliders” (Oxford Encyclopedia, 2023);
DOI: 10.1093/acrefore/9780190871994.013.118
e+e,−μ+μ− Linear
10 PeV
Main Limits:
Power… 3 TWh/yr
Cost….. 3 xLHC
1 PeV
Tevatron
LHC
pp circ.
μμ circ.
linear lepton

## Slide 73
  Thanks for Your Attention !
Questions !?

## Slide 74: Literature
V.Shiltsev, F.Zimmermann, Modern and Future Colliders (Rev.Mod.Phys., 2021)
https://journals.aps.org/rmp/abstract/10.1103/RevModPhys.93.015006
V.Lebedev, V.Shiltsev, Tevatron Book
https://indico.cern.ch/event/774280/attachments/1758668/2915590/2014_Book_AcceleratorPhysicsAtTheTevatro.pdf
W.Herr, CAS school
https://cds.cern.ch/record/941319/files/p379.pdf
Proc. 2013 ICFA mini-workshop on "Beam-Beam Effects in Hadron Colliders"
https://indico.cern.ch/event/189544/
Comprehensive JUAS-book (2371 pages – all topics!)
https://doi.org/10.23730/CYRSP-2024-003.

## Slide 75: ENERGY: Brute Force Approaches
Particle Energy Increase
ΔE = Electric Field Gradient x Length
#1 Increase length = linac
(linear accelerator)
#2 Accelerate in a ring (Nturns ΔE) increase circumference as E=0.3BR
(synchrotrons)

## Slide 76: CCC=CERN Control Center
Over 100,000 signals are generated by the cryogenics, machine protection and beam monitoring systems.

## Slide 77: Further Reading on Accelerator Physics
An Introduction to Particle Physics High Energy Accelerators, D. Edwards and M. Syphers (John Wileyand Sons, Inc, 1993)
Accelerator Physics, S.Y. Lee (World Scientific, 1999)
Hand Book of Accelerator Physics and Engineering – Eds. A. Chao and M. Tinger , World Scientific (1999)
CAS CERN Accelerator, Accelerator Physics Courses http://cas.web.cern.ch/
Accelerator Physics at the Tevatron Collider - by V.Lebedev and V.Shiltsev, Springer (2014)

## Slide 78: Luminosity and Burn-Up
The relationship of the beam to the rate of observed physics processes is given by the “Luminosity”
Rate
Cross-section (“physics”)
“Luminosity”
Standard unit for Luminosity is cm-2s-1
Example: total p-p inelastic+elastic cross section at 13 TeV cme is ~110 mbarn (58 inel+ 12 ssd+40 el not seen)
~60 interactions per crossing x
40,000,000 collision/sec= 2.4e9 protons leave each beam every second
Beam lifetime due to such “Burn up” T=N/(dN/dt)= 2.8e14 protons/(2.4e9/s) =32 hours

## Slide 79
26 658.883 m
6.5 TeV x 2

## Slide 81: Squeeze in ATLAS/CMS
Image courtesy John Jowett
in the arcs:
β~200m, σ≈0.23mm
Numerical Example: LHC (γ »1, β=v/c ≈1)
β* | Sigma*
25 cm | 8 um
βtriplet | Sigma triplet
~5 km | 1.1 mm
σ’=32μrad
σ’=0.14μrad
Ɛn = 1.8 mm·mrad

## Slide 82: Luminosity Lifetime and Integral
2x(1/32+1/32 + 1/110) hrs-1
=14%/hr (7 hrs lifetime)
Take into account two IPs (ATLAS, CMS and 3% LHCb) 1/32+1/32 hrs-1
Take into account beam gas 1/110hrs-1 and that Lumi~N^2  x2

## Slide 83: (Very) Brief History of Colliders
Notable machines and most notable effects/discoveries/breakthroughs
Note that we later will consider in detail:
  LEP, KEK-B and Super-KEKB (lecture VS6)
  Tevatron (lecture VS7)
  LHC and HL-LHC (lecture VS8)
  RHIC and EIC (lecture VS9)
  SLC and linear colliders (lecture VS12)

## Slide 84: Collider Patent R.Wideroe Sept. 8, 1943

## Slide 85: First Colliders
AdA (Frascati/Orsay)
e+e- 500 MeV, ~May1964
VEP-1 (Novosibirsk)
e-e- 320 MeV, May 19, 1964
CBX (Stanford/Princeton)
e+e- 1050 MeV, ~Mar1965

## Slide 86: The First “Trio” of Colliders
Technological challenges addressed:
  development of nano-second-fast injector kickers
  attainment of an ultrahigh vacuum of about a micropascal or better
  reliable luminosity monitoring and other beam diagnostics
Beam physics advances:
  Touschek effect (low energy beam losses due to particle scattering inside beam leading to e+e- gettinbg out of RF buckets)
  luminosity degradation due to beam-beam effects at ξx;y ∼ 0.02–0.04
  complex beam dynamics at non-linear high-order resonances
  coherent instabilities due to resistive vacuum pipe walls

## Slide 87: 1970s-80s “small” e+e- (C=20…200 m)
ADONE (INFN, Frascati)
SPEAR (SLAC, Stanford)
DORIS (DESY, Hamburg)
VEPP-2 (INP, Novosibirsk)

## Slide 88: 1970s-80s “small” e+e-
Technological challenges addressed:
  longitudinal phase feedback system developed and installed (ADONE)
  7.5 T SC wiggler to decrease the damping time (VEPP-2M)
Beam physics advances:
  Luminosity scaling in SR dominated beams (ADONE)
  Sokolov-Ternov effect: the buildup of electron spin polarization through synchrotroton radiation (VEPP-2 and ACO)
  CEA: first time a low-beta insertion optics with a small βy ≈ 2.5 cm
  SPEAR: Transverse horizontal and vertical head-tail instabilities were observed and suppressed a positive chromaticity Q’>0
  DCI: first four-beam compensation attempt (limited success)
  dE/E~10-5 resolution via resonant depolarization method (VEPP-2M)
  Multibunch, e.g. 480 bunches in each ring in DORIS

## Slide 89: 1980s-90s “large” e+e- (C=2…27 km)
PETRA (DESY, Hamburg)
SLC (SLAC, Stanford)
LEP (CERN)
TRSITAN (KEK, Japan)

## Slide 90: 1980s-90s “large” e+e-
Technological challenges addressed:
  SLC: first ever (and only) linear collider – many subsystems
  pioneer SRF technology - TRISTAN: 508 MHz 0.4 GV/turn; LEP 352 MHz SC niobium-on-copper cavities, 3.5 GV/turn
  High current positron sources, incl. 80% polarized e- (SLC)
Beam physics advances:
  LEP: losses via e+/e- scattering off thermal photons in RT beampipe
  LEP single-bunch current limited by TMCI at injection energy
  LEP: beam-beam record tune shift 4xξy=0.33
  SLC : BNS (Balakin-Novokhatsky-Smirnov) damping of BBI
  SLC: ~x2 increase of luminosity due to disruption enhancement @IP

## Slide 91: 2000s-now “factories” e+e- (Φ-, Charm-, B-meson)
PEP-II (SLAC, Stanford)
KEK-B  SuperKEKB (KEK, Japan)
CESR (Cornell)
BEPC (Beijing)
DAΦNE (INFN, Frascati)
VEPP-2000 (BINP, Novosibirsk)

## Slide 92: 2000s-now “factories” e+e-
Technological challenges addressed:
  HV electrostatic orbit separation for e+e- (CESR)
  Efficient SRF for Ampere-class currents, HOM damping
  Asymmetric rings – KEK-B, PEP-II, Super-KEKB
  Tight detector background control - vacuum and collimation
  Since PEP-II/KEKB: top-up injection mode of operation
Beam physics advances:
  Advanced optics for tight vertical focusing with βy ~1cm – few mm
  VEPP2000 : “round beams” concept ξ ∼ 0.25
  (less successful) CESR “Moebius ring” collider scheme (x-y flips)
  DAΦNE : “crab waist” focusing optics, demo “wire b-b compensation”
  KEK-B: crab crossing (limited success)  nonobeams (Super-KEKB)

## Slide 93: 1970s-2010s Hadron Colliders (C=1…7 km)
Tevatron (FNAL, Batavia)
SPPS (CERN)
HERA (DESY, Hamburg)
ISR (CERN)

## Slide 94: 1970s-2000’s Hadron Colliders (1)
Technological challenges addressed:
  ISR: world’s first pp collider (and pp Lumi record holder for >20 yrs)
  SC NbTi magnets 4-8 T (Tevatron  HERA RHIC  LHC)
  SPPS, &Tevatron: technology of antiproton production & scienc of stochastic (Nobel prize) and electron cooling (up to 4 MeV e-)
  Tevatron: permanent magnets (3.3 km 8 GeV Recycler)
  Two-stage collimation systems (HERA, Tevatron)
Beam physics advances:
  Longitudinal manipulations : momentum stacking (ISR), slip-stacking and momentum mining (Tevatron)
  Tevatron: beam-beam record at ξx;y ∼ 0.025, first successful demo b-b compensation by electron lenses, hollow e-lens collimation
  HERA: first e-p collider, transversely polarized e- & spin rotators to l

## Slide 95: 2000s-now Hadron Colliders (C=4…27 km)
RHIC (BNL, Brookhaven)
LHC (CERN)

## Slide 96: 2000s-now Hadron Colliders (2)
Technological challenges addressed:
  First use of Nb3Sn SC magnets (HL-LHC)
  Three (4) stage 99.99% efficient collimation system (LHC)
  Ions sources and ion-ion, ion-p collisions (RHIC, LHC)
  Sophisticated polarization control along the chain (55% in RHIC)
Beam physics advances:
  RHIC: bunched beam stochastic cooling, bunched beam electron cooling
  RHIC: head-on beam-beam compensation with electron lenses
  LHC: sophisticated control of electron-cloud and other instabilities
  LHC: novel achromatic telescopic squeeze optics to lower beta*
  LHC: demo wire compensation of long-range beam-beam effects

## Slide 97: Super-Colliders That Were Not (1990’s)
SSC (Waxahachie, TX)
UNK (IHEP, Protvino)

## Slide 98: Colliders That Will Be
BINP C/Tau-Factory
(Novosibirsk)
NICA (JINR, Dubna)
EIC (BNL, Brookhaven)

## Slide 99: Colliders That Might Be : Higgs factories proposals
CepC/FCCee
100 km
CLIC NCRF 72 MV/m
11 km
ILC SRF 31.5 MV/m
21 km
100MW RF

## Slide 100: Far-Future High Energy Collider Concepts/Proposals
μ+μ- 10-14 TeV cme
10-14 km, 16 T magnets
CLIC e+e- 3 TeV, 100 MV/m 50 km
pp 100 km : SPPC 75 TeV, 12 T magnets, FCChh 100/16 T

## Slide 101: Luminosity Demand : Leptons
need L ~ s ~ E2

## Slide 102: Hadron Cross Sections – Inclusive vs Parton