## Slide 1: 2025 Summer School μ+-μ- Collider Front End
David Neuffer

## Slide 2: 0utline
Muon Collider Front End
  General introduction
    Muon Collider scenarios
    Early versions  MAP  IMCC 
  Capture and decay from target
  Bunching and φ-E rotation
  Match into Initial Cooling

## Slide 3
2023 P5 Report – 2025 NAS recommendation
Muon Fever ?

## Slide 4: Muon Collider Evolution 1979-2015
“difficult but perhaps not impossible”

## Slide 5: Collider development 198319942014 (MAP)
Proton Driver
  RCS  Linac + Storage rings
Front End & Cooling
Li lens -> solenoids
> ring coolers > rectilinear
Acceleration
  RCS 
  Recirculating Linacs 
  Rapid Cycling Hybrid Synchrotrons
Collider
  4 TeV  10 TeV
    8T  ~16 T

## Slide 6: MAP  IMCC versions
Front End –protons  captured muon bunches

## Slide 8: Muon Collider Layouts ~3—10 TeV

## Slide 9: π capture from target
Protons on target produce large number of π’s
  Broad energy range (0 to 10+GeV)
  More at lower energies
  Transverse momentum
  (up to ~0.3GeV/c)
Capture beam from target
Options:
  Li lens
  Magnetic horn
  Magnetic Solenoid

## Slide 10: Front end goal
Take Broad π distribution from target
  Capture transversely
    Transverse focusing
  Capture longitudinally
    Start with short proton bunch
    Drift to develop z-E correlation (πμ + ν)
    Use “RF” to reduce Energy Spread
    30 MHz

## Slide 11: Proton Driver
Intense proton bunches (L < ~1 m)
PIP-II Fermilab or CERN SPL
RCS solutions possible
  J-PARC can deliver similar bunch intensities
5--10 GeV H- Linac

## Slide 12: Target needed (Zwaska)
Target must accept ~ 2 -4 MW beam at 5—10 Hz
  ~0.5 MJ pulses
Target Options
  C – Graphite targets
    He cooled ?
  Heavy Liquid Metal (Pb/Hg/?) & fluidized W targets
  Or ???

## Slide 13: Solenoid lens capture
Target is immersed in high field solenoid
Particles are trapped in Larmor orbits
  Produced with p = p‖, p
  Spiral with radius r = p/(0.3 Bsol)
  Particles with p < 0.3 BsolRsol/2 are trapped
  p,max < 0.225 GeV/c for B=20T, Rsol = 0.075m
  Focuses both + and - particles

## Slide 14: Solenoid transport
Magnetic field adiabatically decreases along the transport
Transverse momentum decreases
  Busch’s theorem: B rorbit2 is constant
  B=20T→2T (r=3.75cm →= 12cm)
  P = 0.225→0.07GeV/c
Emittance = ~σx σpx/105.66
  ~6cm×35 MeV/c/105.66≅0.02m
P remains constant (P‖ increases)
Transport designed to maximize π→ acceptance

## Slide 15: Homework problem
How many 10 GeV protons per second are in a 4 MW beam? With 5 Hz bunches, how many protons/bunch?
If beam of 10 GeV protons produces, on average, one pion pair per proton with mean momentum of 250 MeV/c (per pion), what percentage of the proton beam kinetic energy is converted to pions?
If the target is surrounded by a 20T solenoid with a 5 cm radius aperture, what maximum transverse momentum of pions is accepted?
If B is adiabatically reduced to 2.5T what is the resulting transverse momentum and beam orbit size?

## Slide 16: Longitudinal Capture Phase-energy rotation
Beam is initially short in length
  Bunch on target is 1 to 3 ns rms length
As Beam drifts down beam transport, energy-position (time) correlation develops:
Goal:
  Accelerate “low-energy tail”
  Decelerate “high-energy head:
  Obtain long bunch
    with smaller energy spread
Requires rf
  Single bunch – low-frequency rf 10MHz
  Multi bunch high-frequency rf
L=1m
L=112m
rf
0
0.5GeV/c
-50m
50m
dL

## Slide 17: Adiabatic Buncher overview
Want rf phase to be zero for reference energies as beam travels down buncher
Spacing must be N rf rf increases (rf frequency decreases)
Match to rf= ~1.5m at end:
Gradually increase rf gradient
(linear or quadratic ramp):
Example: rf : 0.901.5m

## Slide 18: Adiabatic Buncher example
Adiabatic buncher (z=90→150m)
Set T0, :
  125 MeV (205.04 MeV/c), 0.01
In buncher:
Match to rf=1.5m at end:
zero-phase with 1/ at integer intervals of  :
Adiabatically increase rf gradient:
rf : 0.901.5m

## Slide 19:  Rotation
At end of buncher, change rf to decelerate high-energy bunches, accelerate low energy bunches
Reference bunch at zero phase, set rf less than bunch spacing
(increase rf frequency)
Place low/high energy bunches at accelerating/decelerating phases
Can use fixed frequency (requires fast rotation) or
Change frequency along channel to maintain phasing “Vernier” rotation –A. Van Ginneken

## Slide 20: Fast “Vernier”  Rotation
At end of buncher, choose:
  Fixed-energy particle T0
  Second reference bunch TN
  Vernier offset 
Example:
  T0 = 125 MeV p=205 MeV/c
  Choose N= 10, =0.1
  T10 starts at 77.28 MeV p=150MeV/c
  Along rotator, keep reference
  particles at (N + ) rf spacing
  10 = 36° at =0.1
  Bunch centroids change:
Use Erf = 10MV/m; LRt=8.74m
  High gradient not needed …
  Bunches rotate to ~equal energies.
rf : 1.4851.517m in rotation;
rf = ct/10 at end
(rf  1.532m)
Nonlinearities cancel:
T(1/) ; Sin()

## Slide 21: “ICOOL” Adiabatic  Rotation
At end of buncher, choose:
  reference particle T0
  Reference bunch TN (N bunches from 0)
  V’ rf gradient, offset N
Example:
  T0 = 125 MeV
  Choose N= 10, N=0.1
    T10 starts at 77.28 MeV
In ICOOL
  T0 = T0 + E0'z…
  TN =TN + EN' z
  Rotate until T0 ≅ TN
Along rotator, keep reference particles at (N + N) rf spacing
  EN' ≅eV' sin(2π)
λrf ~1.4 to 1.5 m over rotation
~Adiabatic
Particles remain in bunches as bunch centroids align
Match into 201.25 MHz Cooling System

## Slide 22: Simulation results
50m
-50m
0
0.5
GeV/c

## Slide 23: High-frequency Buncher +  Rotation(2011)
Drift (80m)
  Allows  beam to decay;
  beam develops  correlation
Buncher (~333230MHz)
  Bunching rf with E0 = 125 MeV, 1 = 0.01 { L  1 =~1.5m at Ltot = 150m}
  Vrf increases gradually from 0 to ~6 MV/m
 Rotation (~233200MHz)
  Adiabatic rotation
  Vrf =~10 MV/m
Cooler(~100m long) (~200 MHz)
  fixed frequency transverse cooling system
Replaces Induction Linacs with medium-frequency rf (~200MHz) !
Captures both μ+ and μ- !!
18.9 m
~60.7 m
FE Target
Solenoid
Drift
Buncher
Rotator
Cooler
~33m
42 m
~80 m
p
π→μ

## Slide 24: MAP-325 MHz System
Drift
  20T 2T
Buncher
  Po=250MeV/c(1/β = 1.08564)
  PN=154 MeV/c(1/β= 1.2127); N=12
  Vrf : 0 15 MV/m
  fRF : 490 365MHz
Rotator
  Vrf : 20MV/m
    (2/3 occupied)
  N=12.045
  P0, PN245 MeV/c
Cooler
  FOFO, 325 MHz, 25 MV/m
  2 1.5 cm LiH absorbers
  /0.75m

## Slide 25: Variation to control losses
Initial front end was open from target to cooler
  Accepts μ+, μ- at ~250 MeV/c
  Also accepts everything else
  - p, e+-
Introduce chicane + absorber to filter out unwanted particles (C. Rogers, et al.)
  Chicane cuts out P > 500 MeV/c
  Absorber stops protons, electrons, pi, ….
    10 cm Be
absorber

## Slide 26: 325 “Collider “ w Chicane/Absorber
Readjust parameters to correct for chicane/absorber
Add 30 m drift after chicane
  *6.5m  +21.67°,-21.67º
Add chicane + absorber
    particle 1-283 MeV/c, particle 2-194 MeV/c
  absorber at 54m
    10cm Be
    particle 1-250 MeV/c, particle 2-154 MeV/c
  Bunch (N=12) 015 MV/m :490 365 MHz
  Rotate (N=12.045 )– 20MV/m : 365  326.5 MHz
  Cool -325MHz -25 MV/m
    pref=245 MeV/c
Chicane + Absorber

## Slide 27: Compare without/with chicane
0 GeV/c
1600 GeV/c
0m (production target)
66m (after chicane/absorber)
88m (after drift)
109m (after buncher)
132m (after rotator)
190m (after cooling)
-30m
50m
0m
57m
79m
102m
152m
1600 GeV/c
0 GeV/c
-30m
-50m
21 bunches for Collider

## Slide 28: Rf Buncher/Rotator requirements
Buncher -21m
  37 cavities (14 frequencies)
  13 power supplies (~1—3MW)
RF Rotator -24m
  64 cavities (16 frequencies)
  20 MV/m, 0.25m
  ~2 MW (peak power) per cavity
Cooling System – 325 MHz
  200 0.25m cavities (75m cooler), 25MV/m
  ~4MW /cavity
Front End section | Length | #rf cavities | frequencies | # of freq. | rf gradient | rf peak power requirements
Buncher | 21m | 42 | 484 to 365 | 14 | 0 to 16 | 0—1.34 MW/cavity
Rotator | 24m | 56 | 364to 326 | 16 | 20 | ~2.4 MW/cavity
Cooler | 75m | 200 | 325 | 1 | 25 MV/m | ~3.7MW/cavity
Total df+bxr+rttr | ~134m | 93 |  | 30 | ~500MV | 140MW
6-D cooler | 126m | 360 | 325 MHz | 1 | 25 MV/m | ~3.7 MW

## Slide 29: Simulation Results
N :0.15<P<0.35 GeV/c
N: εT<0.03; AL<0.2
N: εT<0.015; AL<0.2
Simulation obtains
  ~0.12 μ/p within acceptances
FOFO cooling
  Cools transversely
  By factor of 3
    ~10 in 6-D
Useful
cooling

## Slide 30: Optimization (H. Kamal Sayed)
Buncher +Rotator-31 cavity sets
  Changed frequency, rf gradient
Optimized using NERSC supercomputer using evolutionary optimization algorithm, 100’s of simulations
  Increase Erf in Buncher
    By ~4 MV/m
    Higher gradient better
  Rf reaches 325 MHz faster …
    Could use shorter system ?
    Could start further downstream
H. Kamal Sayed, NIM A 794 (2015) 193–199
Buncher
Rotator

## Slide 31: 4-D6-D cooler
Initial version had transverse-only cooler
  FOFO 4-D cooler
Alternative:Helical FOFO snake
  Alternating tilted solenoids
126 m long
  2 cavities every 0.7m
  160 0.25m cavities 25 MV/m
Cools longitudinally and transversely
  L  1/3, 1  1/6 , 2 1/5
  ~1/100  (6-D cooling)
Cools both + and -

## Slide 32: Summary Front End Design
Buncher/Rotator scenario parameters developed semiempirically
  Guided by simulations, extrapolation, intuition
  Some optimization
IMCC design uses Buncher-Rotator
  Has not been reoptimized and rematched in current scenario
Needs reassessment and optimization

## Slide 33: Update for IMCC, US MCC
Has not yet been reoptimized for IMCC
  352, 704 MHz cooling system
  Front end: 325 MHz  352 MHz
    Smaller apertures ?? –start at ~500 MHz
  Consider 176 MHz Front end ? (C. Rogers)
    Initial cooling at 176 MHz ?
Has not been optimized in General
  2015 optimizations not yet implemented
  US MCC version ?

## Slide 34
Thank you
for your attention

## Slide 35: Scenario Construction
Parameters available in ICOOL constrain method
Start with final rf frequency
  325 MHz
Select 2 reference particles
  Initial momentum 250 MeV/c / 180 MeV/c (δ(1/β))
Select number of bunches, end of drift
  n = 12, Lo= 60 m?
Buncher length, rf gradients
  21 m 016 MV/m
Rotator length, rf gradient
  N =12.05, 24m, 20 MV/m
  Icool parametrization not ideal
    Ref particle accelerations  245 MeV/c
Adjust lengths to match
Match to cooling

## Slide 36: 325MHz System for Collider”
Drift
  20T 2T
Buncher
  Po=250MeV/c
  PN=154 MeV/c; N=12
  Vrf : 0 15 MV/m
  fRF : 493 365MHz
Rotator
  Vrf : 20MV/m
  fRF : 364 326MHz
  P0, PN245 MeV/c
Cooler
  245 MeV/c
  325 MHz
  25 MV/m
  2 1.5 cm LiH absorbers
  /0.75m

## Slide 37: Summary slide