## Slide 1: Recent Developments in RF Cavities with Beam Windows for the Future Muon Collider Ionization Cooling Channels
Dillon Merenich (NIU), Tianhuan Luo (LBNL), Xueying Lu (NIU/ANL) 8 August 2025

## Slide 2: Overview
Motivation
Emittance Dilution Trade Study
Breakdown Resilience of Different Materials
Wakefield Studies of Enclosed Cavities
Conclusions
Future Plans

## Slide 3: Cooling Channel RF Cavities
https://cds.cern.ch/record/2913567/files/document.pdf
Example cavity design from CERN

## Slide 4: Scattering Simulation Setup Using GEANT4

## Slide 5: Phase Space Samples for Muon Collider Stages
Stages considered: A1, B1, and B10
Particle loss is negligible
A1 Be phase spaces scattered on 3 μm
B1 Be phase spaces scattered on 3 μm
B10 Be phase spaces scattered on 3 μm
y(mm)-
x(mm)
px(MeV/c)-
x(mm)

## Slide 6: Emittance Dilution Comparison Between Early and Late Stages
As expected, earlier stages have larger emittance, so the emittance dilution effect is small
At later stages, Al will require ¼ thickness to achieve similar emittance dilution as Be
Although changes are small, multicell channels will scale these effects by number of cavities

## Slide 7: Temperature Dependent Breakdown Model in a Magnetic Field
Effects of external magnetic fields on the operation of high-gradient accelerating structures - ScienceDirect
Temperature change threshold
Heat conduction
FN Current density
Temperature Rise
D. Stratakis et.al 2010

## Slide 8: Previous Studies of the Breakdown Threshold
Previous studies assess results for Be, Al, and Cu 🡪 Be shows dominance due to its low density and large temperature threshold
Inspired by recent scaling studies 🡪 alluded to cold copper with limited improvement
https://indico.cern.ch/event/1043014/contributions/4382434/attachments/2255971/3827989/Scalings_with_T_and_f.pdf
Sergey Arsenyev 2021

## Slide 9: This Work: Adding thermal diffusion and Thermal-mechanical changes
Investigate the effects of both thermal and reduced current changes for cold Cu
  Thermal diffusivity, thermal conductivity, and thermal expansion
805 MHz cavity assumed
Higher magnetic fields
Note: all results evaluate at r,z = 0

## Slide 10: Cold Copper Temperature Dependent Breakdown Resilience
When considering thermal changes and the reduced current, cold copper has better resilience at higher magnetic fields
  Be and Al have higher temperature rise thresholds 🡪 when low power is deposited, they outperform
  At high magnetic fields, cold Cu’s reduced field emission and enhanced diffusivity provides resilience to temperature change, and thus BD

## Slide 11: Previous Study Pulse Lengths Effects on Breakdown
Pulse length reduction shown to mitigate effects of breakdown
Temperature rise scales linearly without diffusion
https://indico.cern.ch/event/1034749/contributions/4345479/attachments/2243084/3803574/02%20-%20Overcoupled%20cavity%20v4.pdf
Sergey Arsenyev 2021

## Slide 12: Pulse Length Effects of room temp copper
At large magnetic fields, the pulse lengths required to avoid diffusion are very small
To increase diffusion limits at large magnetic fields
  Use material with enhanced diffusivity
  Decrease pulse lengths at larger magnetic fields

## Slide 13: Beam Loading Overview
Wake function describes the energy loss per trailing charge per bunch charge
    Couples to high R/Q modes
    Combination of cavity modes and space charge effects
    Green’s function of wake potential for bunch distribution
  Decomposition of fields due to linear addition of particle and structure fields
    MuC particle beta ~ 0.9 🡪 space charge relevant
Particle Bunch
https://arxiv.org/pdf/physics/0309023
Wakefield Decomposition
Single Particle

## Slide 14: Wakefield Simulations in a Simple Pillbox with Beam Pipe
C/s
C
GHz
ns

## Slide 15: Wakefields in a Simple Pillbox with Beam Pipe
Pipe insertion does impact the resulting beam loading effects

## Slide 16: CST PIC Solver - Setup
Mimic bunch charge from wakefield solver
Extend pipe to remove edge effects, valid since wakefield solver uses open bounds
Resolve fields and export
Calculate wake potential in post processing w/ Python
PIC model
Beam center

## Slide 17: Wakefield Results Using CST PIC – Pillbox with a Pipe
Wakefield model
rp=25mm, d=12mm
β=1
β=0.9
Perfect agreement between postprocessing and Wakefield Solver

## Slide 18: Space Charge Wake Reflections
At larger radii, the space charge wakes from a smooth pipe are reflected at the open boundaries

## Slide 19: PIC Results of An Enclosed Pillbox
3-segmented PIC setup
Wakefield Results

## Slide 20: Conclusions
Scattering Studies
  Assessed emittance dilution for Al and Be
  Al needs to be ~1/4 the thickness of Be to achieve same emittance values
Breakdown Studies
  Cold copper shows strong breakdown resilience due to its enhanced diffusivity
  Pulse length reduction can improve breakdown resilience within diffusion limits
Wakefields studies
  CST Wakefield solver is not sufficient to study beam loading for enclosed cavities 🡪 beam pipe is required
  CST PIC solver with post processing can resolve wakefields for specific cases but there are instabilities with boundaries
    Anticipated wakes on the order of MV/m, comparable to beam gradients

## Slide 21: Future Plans
Simulate vacuum vessel changes for Wakefield studies
Assess copper alloys (e.g. CuAg) to mitigate breakdown
Test true RF pulse envelopes (rise, flattop, and decay)

## Slide 22: Acknowledgements
Dr. Omkar Ramachandran (NIU) for discussions regarding code developments
Dr. Carmelo Barbagallo (CERN) for helpful discussions and collaborative insights on wakefield studies
IMCC-RF working group
Funded by the DoE SCGSR program contract number DE‐SC0014664, DoE Contract No. DE-AC02-05CH11231,and DoE Awards DE-SC0021928 and DE-SC0022010.

## Slide 23: Thank You! Questions or comments?

## Slide 24: Material Dependence of Scattering in Thin Windows
Charged particles incident upon a material interact with the atoms inside of the material 🡪 transverse spreading and energy loss
Parameters relevant for this study are material and particle energy dependent
  Material density
  Atomic mass and mass numbers
  Particle energy
Plane rms scattering angle
Bethe-Bloche energy loss due to scattering

## Slide 25: Backup: MuC Stages
https://arxiv.org/pdf/2409.02613v1

## Slide 26: Parameters for Muon Collider Stages
Stages considered: A1, B1, and B10
Average particle losses for all stages ~ 17+-3

## Slide 27: 1D Bunch Wake Validation, radius = 5 mm

## Slide 28: 1D Bunch Wake Validation, radius = 25 mm

## Slide 29: 1D Bunch Wake Validation, radius = 50 mm

## Slide 30: 1D Bunch Wake Validation, radius = 120 mm

## Slide 31: Muon Collider Stages Comparison to Theory
Strong agreement with theory 🡪 discrepancy from averaging over all energies and statistical variation
In all cases, from a pure scattering angle perspective, Al windows need to be about 1/4 to that of the Be

## Slide 32: Backup: BD in a Field
Effects of external magnetic fields on the operation of high-gradient accelerating structures - ScienceDirect
Temperature threshold
Heat conduction
FN Current density
Heat/unit area
Final radius
Temperature Rise

## Slide 33: Previous Studies Ignore Temperature Dependent Properties
https://indico.cern.ch/event/1043014/contributions/4382434/attachments/2255971/3827989/Scalings_with_T_and_f.pdf
Yield strength changes negligible
Therm. exp. and Cp changes cancel

## Slide 34: Previous Studies Considered Reduced Current at low T
https://indico.cern.ch/event/1043014/contributions/4382434/attachments/2255971/3827989/Scalings_with_T_and_f.pdf
Field enhancement correlates to factor ~100 current reduction at 77k

## Slide 35: Cold Copper Superior Breakdown Resilience w/o B-field
Cold copper shows higher breakdown resilience in recent SLAC experiments at X-band
High gradient experiments with -band cryogenic copper accelerating cavities | Phys. Rev. Accel. Beams

## Slide 36: Backup: Breakdown Threshold
System is constrained to strain values are 0
Solving for an individual sigma yields

## Slide 37: Breakdown in a B-Field
Here we investigate the effects of both thermal and reduced current changes for cold Cu
We also look into higher magnetic fields

## Slide 38: BackUp: Cold Cu Temps

## Slide 39: BackUp: Temps

## Slide 40: BackUp: All SOG

## Slide 41: Diffusion Limit of Solution
At early time steps, the heat from early sources has not spread (r, z = 0)
  Linear growth region

## Slide 42: Decay of Temperature after pulse length