## Slide 1: Multi-physics Approach in the Design and Optimization of Muon Cooling Cavity
Zenghai Li, SLAC
2nd Annual US Muon Collider Collaboration Meeting, August 7-8, 2025
University of Chicago, Illinois

## Slide 2: Outline
SLAC’s past involvement in the muon collider program
ACE3P multiphysics modeling suite
805-MHz cavity design improvement using ACE3P
805 MHz modular cavity design and Multiphysics analysis
ACE3P newly added modeling capabilities
Outlook

## Slide 3: SLAC’s Past Involvement in MAP
805 Pillbox cavity
201 MHz cavity
805 MHz modular cavity
Cavity operates under strong magnetic fields
Issues
Significant surface damage due to field emission and multipacting currents
Approach
Analyze field emission and MP
RF design mitigation
Tools - ACE3P
Omega3P
S3P
Track3P

## Slide 4: Electron Trajectories Under Strong External Magnetic Field
Electron trajectories follow external magnetic field

## Slide 5: RF Challenge – 805 MHz cavity
Significant degradation in maximum stable operating gradient with applied B field
Significant damage observed
  Iris
  RF coupler
However
  No damage to Be window
805 Pillbox Post-Mortem
E field

## Slide 6: Motivation and Approach
  to better understand potential impacts of surface fields on performance under a strong external magnetic field
  massively parallel computing using finite element ACE3P tools on NERSC supercomputers

## Slide 7: ACE3P Modules and Multiphysics Modeling Capabilities
Omega3P (Frequency domain)
  Real eigenmodes in lossless or periodic cavities
  Complex eigenmodes in lossy or externally loaded cavities
  Mode damping in dielectric and ferrite materials
  Linear, quadratic and nonlinear eigensolvers
  Periodic, absorbing and PML boundary condition
  S-parameters of rf components and open structures
  Dipole excitation
  Dielectric and ferrite materials
  Effects due to surface impedance on conductor walls
  Absorbing and PML boundary condition
  Boundary condition for thin coating layer
S3P (Frequency domain)
  Integrated EM, thermal and mechanical effects
  Nonlinear thermal and electrical conductivities
  Convective boundary conditions
  Shell elements for surface coating
  Mechanical eigen and harmonic solvers
  Transient analysis
TEM3P (Thermal & Mechanical)
  Transient and wakefield from source excitation
  Moving window technique for broadband pulse and short beam propagation
  Absorbing and PML boundary conditions for far fields
  Impedance boundary condition for thin coating and lossy conductor walls
  Nonlinear materials
  Self consistent particle-in-cell (PIC)
  User-specified particle emission model
T3P/Pic3P (Time domain)
  Particle tracking code in external rf and static fields
  Multipacting and dark current in rf cavities and components
  Surface physics for field and secondary emissions
  Enhancement counter for multipacting
Track3P (Particle tracking)
Gun3P (Static PIC)
  DC gun modeling at steady state
  Space-charge limited emission
  Electrostatic solver
  Magnetostatic solver
  Particle tracking in external and self static fields
Recent developments

## Slide 8: 805 MHz Cavity Design Improvement – Omega3P
Slot 1
slot 2
end bp
anose
E
B
Original
New low field design
E
B
New with window
E
B
Low Surface Field

## Slide 9: Multipacting and Field Emission Simulation - Track3P
3D parallel high-order finite-element particle tracking code for dark current and multipacting simulations
MP simulation process
Electrons are launched from specific surfaces over a full RF period.
Track electrons for a specified number of RF cycles
Identify resonant trajectories, determine the multipacting order (#cycles/impact) and type (#impact positions/MP cycle)
Calculate enhancement counter or using SEY curve to determine MP strength
Copper SEY curve
Sample MP trajectories in various RF components
Coax line with partial standing wave
TTF-III coupler between window and inner conductor
Equator of elliptical cavity

## Slide 10: Multipacting Analysis with External Magnetic Field – Track3P
850 MHz pillbox cavity
Field level scan: 0.1MV/m – 30MV/m, interval 0.1MV/m
Initial Particles distributed on all exterior surface
Each field level ran 50 RF cycles
3 Tesla
Original Design
New Design
Window
Disk rounding
Coupling iris
Other

## Slide 11: Field Emission Dark Current Analysis – Track3P
Window
Disk rounding
Coupling iris
Field emission current corresponding to surface E field

## Slide 12: Modular Cavity
Modular Cavity (2013)
Modular
Cavity
Pillbox Cavity
[Daniel Bowring]

## Slide 13: Modular Cavity Design and MP Mitigation – Omega3P/S3P/Track3P
B=0T
cavity outer wall
coupler neck
B=3T
Coating Area

## Slide 14: Modular Cavity Thermal & Stress Analysis – TEM3P
Stainless Steel
Copper ring
Beryllium wall
Stainless steel with copper coating inside
 | Emax | σ for Beryllium | Duty Factor | Cooling channel Temperature | ΔT on Be Window
Case 1 | 25 MV/m | 2.33e7 S/m | 0.001 | 25 °C | ~4 °C
B Field
(RF heating only, beam heating not included)

## Slide 15: Modular Cavity High Power Test (Daniel Bowring)

## Slide 16: Radiation Heating Modeling – TEM3P
LCLS-II Beam Dump
FLUKA or Geant4 dose map
beam
Stress
Temperature
Volume radiation heating integrated to TEM3P for
Evaluating Radiation Effect on Cavity and surrounding materials

## Slide 17: Dark Current and Radiation Analysis - ACE3P/Geant4 Integration
Developed an integration simulation tool of ACE3P and Geant4 for dark current radiation analysis.
Implemented a particle data transfer scheme from ACE3P into Geant4
HEP US-Japan Science and Technology Cooperation Program (2022 -2025)
Field emission particle trajectories from Track3P
Radiation pattern from Geant4
KEK measurement
KEK measurement
Track3P
Geant4
Dark current at downstream Faraday cup
In collaboration with KEK

## Slide 18: LUME-ACE3P Workflow for Design Optimization
LUME-ACE3P Outputs
User Inputs
Individual workflow folders
Formatted sweep output file
Python-based data visualization
Run LUME-ACE3P Workflow
LUME-ACE3P config. input file (.yaml)
Optional postprocess file (.rfpost)
ACE3P input file (.s3p or .omega3p)
Cubit journal file (.jou)
LUME - an ecosystem of open-source software tools and standards to enable large-scale start-to-end simulations from particle generation through experimental analysis
LUME-ACE3P - python-based manager for ACE3P workflows, configured for parameter sweeping or optimization
workflow_parameters :
'mode' : 'parameter_sweep'
'module' : 's3p'
'cubit_input' : 'bend-90degree.jou'
'ace3p_input' : 'bend-90degree.s3p'
'ace3p_tasks' : 32
'ace3p_cores' : 4
'ace3p_opts' : '--cpu-bind=cores'
'workdir' : 'lume-ace3p_s3p_workdir'
'workdir_mode' : 'auto'
'sweep_output' : True
'sweep_output_file' : 's3p_sweep_output.txt’
input_parameters :
'cornercut' :
'min' : 12.0
'max' : 16.0
'num' : 5
'rcorner2' :
'min' : 4.0
'max' : 16.0
'num' : 3
demo_s3p_sweep.yaml
Values swept to create folders and update files
Corner chamfer length
Inner corner radius

## Slide 19: Computational Tools for Rapid RF Source Design
Refinement of HPC tools for rapid RF source design. ACE3P is an excellent platform. We are developing an all-in-one code suite with:
  Electrostatic model (for HV standoff)
  Magnetostatic model (for magnet/solenoid design)
  Particle tracking (for gun design)
  Electromagnetic model (for cavity cold testing / tuning)
  Self-consistent Electromagnetic PIC (for large-signal performance)
  Utilization of large machines (HPCs with GPU support)
RF gun model for HEIOT
IEEE Journal on Multiscale and Multiphysics Computational Techniques 4 (2019): 245-259.
Physical Review Applied, 16 (2021): 044040
“Recent Advances in the Accelerator Electromagnetic Code ACE3P,” Proc. 25th IVEC, Monterey, CA (2024)
SLAC Publications on Early-Stage Computational Tools
75XP4 Klystron DC gun
Continue to benchmark, add diagnostics to ACE3P for RF source design, and validate by distributing to the community
Othman, Mohamed

## Slide 20: Novel Design and Large-scale Computing Capability
10M DOF
64M DOF
36M DOF
LHC Crab
HE11 Cavity (LDRD)
C3 Structure
12M DOF
RF Gun
(distributed coupling, cold copper)

## Slide 21: High Performance Computing (HPC) for Solution Speedup
Perlmutter: Cray EX
3072 CPU nodes
1792 GPU nodes
2.2 petabytes of memory
Omega3P w/ 12M DOF’s
T3P w/ 130M DOF’s
National Energy Research Scientific Computing Center
ACE3P has built a broad capabilities for RF design and optimizations that would benefit muon accelerator R&D
New capabilities can be integrated into ACE3P to address new design requirements

## Slide 22: Outlook - What Can We Contribute
RF Cavity design
Mitigation of field emission dark current and multipacting
Thermal and Mechanical Analysis – beam, radiation and RF heating
High power testing – new structure and materials [Emma’s talk]

## Slide 23: Acknowledgement
Computational Electrodynamics Department
  High performance computing code development
  Multiphysics cavity modeling slides (Cho Ng, Lixin Ge, David Bizzozero, Liling Xiao and Mohamed Othman)
  Computing used DOE NERSC computing facilities

## Slide 24: Development Area for Future RF Sources
Othman, Mohamed
Complex Material Systems
Nonlinear materials, frequency Conversion and saturation
Modeling of ceramic windows is instrumental in predicting the nascent stages of operational failures.
Dispersive Media and Time-Dependent material response.
Advanced Beam Dynamics and Mode Composition
Fully self-consistent 3D beam transport and dynamics in output structures, including the effects of periodic permanent magnet (PPM) stacks
Reduction of numerical noise through various techniques
Mode Extraction and Model Reduction
Virtual tuning of klystron cavities for ease of manufacturing tolerancing
Use Dynamic Mode Decomposition (DMD) to reduce complexity and simulation time
Large Signal Models for high power RF Sources
Iterative Tuning for Cavity Optimization
The AI/ML Frontier
Convolutional neural networks (CNNs) to compute
space charge effects and accelerate simulation time.
Nonlinear material response in both transient and PIC solver
Frequency dependent material response
CNN model of high charge density beam in confined magnetic field including space charge
Eigenmode of output structure calculated through DMD
Beam loading calculation in input cavity through PIC simulation